## Slide 1
ArcticDEM
Paul Morin and Mike Cloutier
Polar Geospatial Center
October 26, 2015

## Slide 2
Polar Geospatial Center

## Slide 3
The DigitalGlobe Satellite Constellation
WorldView-2
GeoEye
QuickBird
IKONOS
WorldView-3
WorldView-1

## Slide 4: NSF Funded Polar Researchers See the Arctic Differently
On-demand sub-meter archive imagery and new collection
Orthorectification and mosaicking as required
Terrain is on-request for almost all of both poles

## Slide 5: Terrain Generation Looks Different to PGC
NGA and DigitalGlobe have a huge, high-latitude stereo collection capacity
NSF has high performance computing
100Gbit networking is common in the US
HPC ready DEM extraction software is open source
Storage is cheap

## Slide 6: About NGA Commercial Imagery
Licensed from DigitalGlobe, Inc. for USG purposes.
Resolution of 32-42cm panchromatic and 1.2-1.6m multispectral.
Raw and orthorectified imagery is copyrighted. Derived data (DEMs, NDVI, coastlines) can be freely distributed.
Free to US civilian agencies and federally funded investigators if their sponsoring agency provides an access point.

## Slide 7
EXAMPLE SUPPORT REQUESTS
user services

## Slide 8
EXAMPLE SUPPORT REQUESTS
user services
Fixed Wing Landing Site Support, Tucker Glacier, Antarctica

## Slide 9
EXAMPLE SUPPORT REQUESTS
user services
Summit of Mount Erebus Reference & Planning Map

## Slide 10: ArcticDEM Goal
Produce a 2m posting digital surface model of the Arctic during the US Chairmanship of the Arctic Council using DigitalGlobe stereo imagery licensed by the National Geospatial-Intelligence Agency

## Slide 11: Alaska: Two Meter Resolution Test

## Slide 12: Iceland 2m Test

## Slide 13: Iceland 2m Test

## Slide 14
Reykjavik, Iceland – 2m Digital Surface Model
Coastline provided by the National Land Survey of Iceland, delivered by Tómas Jóhannesson of the Icelandic Met Office
Elevation derived using Surface Extraction with TIN-based Search-space Minimization (SETSM) – M.J. Noh and Ian Howat (Ohio State University)

## Slide 18
STEREO-DERIVED ELEVATION MODELS
Hillshade rendering: Thermokarst collapse, Kuparuk watershed, Alaska

## Slide 19
STEREO-DERIVED ELEVATION MODELS
Hillshade rendering: Okmok Caldera, Umnak Island, Alaska

## Slide 22
Hillshade rendering: Barrow, Alaska - Porter

## Slide 23
STEREO-DERIVED ELEVATION MODELS
Hillshade rendering: The Barnes Ice Cap, Nunvavut, Canada, Noh and Howat

## Slide 24
STEREO-DERIVED ELEVATION MODELS
Hillshade rendering: Unaska Island, Alaska - Morin

## Slide 25
STEREO-DERIVED ELEVATION MODELS
Hillshade rendering: Outlet glacier, west Greenland Noh and Howat

## Slide 26
The ArcticDEM Domain

## Slide 27: Expected Accuracy
Without ground control
  Dependent on the sensor’s Rational Polynomial Coefficients (RPC) accuracy
  WorldView 1 & 2 DTMs have a horizontal positional accuracy of 4m CE90
Using NASA Operation IceBridge LiDAR
  Point accuracy of 0.20-0.35 m (1 standard deviation – accuracy of lidar or DEM after registration)
Ground-survey (e.g. GPS benchmark) control points not yet employed, but tests show similar accuracy to lidar
Myoung-Jong Noh & Ian M. Howat (2015): Automated stereo-photogrammetric
DEM generation at high latitudes: Surface Extraction with TIN-based Search-space Minimization (SETSM) validation and demonstration over glaciated regions, GIScience & Remote Sensing, DOI:10.1080/15481603.2015.1008621

## Slide 28: Basic Statistics
300,000-17x17km scene pairs in the current archive
An 8m posting DEM for one scene pair requires 4 SUs of HPC time
A 2m posting DEM for one scene pair requires an additional 8 SUs of HPC time

## Slide 29: What we need
Your input
Accurate Coastline
Ground Control
  LiDAR
  InSAR Surveys
  Kinematic GNSS Ground Surveys
  Cadastral Points, Leveling and GNSS Locations
  ICESat and Cryosat Altimetry

## Slide 30: What you need to do
Ensure you have bandwidth
Disk space
Look at lots and lots of data
Formulate a strategy to improve data
Figure out if and how you can contribute

## Slide 31: Don’t do significant work before talking to PGC
New data is processed all the time
Possible bugs
New post-processing improvements
New data is being collected and received at PGC

## Slide 32: ArcticDEM Final Products
2m Posting Mosaic of the Arctic
2m Time-stamped Strips

## Slide 34
SUPERCOMPUTING
hardware & infrastructure
Servers at OIT data center wrapped for cooling

## Slide 35: NSF High Performance Computing
About 40,000,000 Core hours Allocated

## Slide 36
g
Cray XE6/XK7 - 276 Cabinets
XE6 Compute Nodes
5,688 Blades – 22,640 Nodes – 362,240 Cores –
724,480 Integer Cores 4 GB per FP core
DSL
48 Nodes
MOM
64 Nodes
esLogin
4 Nodes
Import/Export
28 Nodes
Management Node
esServers Cabinets
HPSS Data Mover
50 Nodes
XK7 GPU Nodes
1056 Blades – 4,224 Nodes
33,792 Cores – 4,224 GPUs
Sonexion
25+PB online storage
144+144+1440 OSTs
BOOT
Nodes
SDB
Nodes
Network GW
Nodes
Unassigned
Nodes
LNET Routers
582 Nodes
InfiniBand fabric
Boot RAID
Boot Cabinet
SMW
10/40/100 Gb
Ethernet Switch
Gemini Fabric (HSN)
RSIP
Nodes
NCSAnet
Near-Line Storage
300+PB
Cyber Protection IDPS
NPCF
Notes: Blue Waters supersystem, Need to emphasize the unprecedented scale. Largest Cray, IE, HPSS, Lustre, Network. Hold performance discussion to later slides. Note all storage sizes are usable storage.

## Slide 46: Stereo Coverage by Year

## Slide 47: US ArcticDEM Partners
National Geospatial-Intelligence Agency
  Manages the DigitalGlobe contract
  Providing data and tasking to NSF/PGC
  Improvement of the Alaska DEMs
  Advise on automated improvement of all DEMs
National Science Foundation
  Providing HPC (Blue Waters/XSEDE and funding to PGC
  PGC will be generating DEMs and managing the project
USGS
  Overall coordination
ESRI and Google
  Data distribution
  Viewers

## Slide 48: PGC’s Contribution
Processing the stereo imagery into DEMs
Tasking to continue to fill holes and continue the time series
Other automated post processing
  Ground control using LiDAR
  Mosaicking
PGC will not manually improve data products

## Slide 49: Next Steps
8m Circum-Arctic test.
Begin development of circum-arctic ground control database
NGA is raising the priority of collection over stereo imagery holes.
All DigitalGlobe arctic stereo is being moved to PGC.
Work with the arctic nations on their contributions including ground control, coastline, DEM improvement, etc.
Work out delivery with ESRI and Google.

## Slide 50: What will happen today
Deeper discussion about the data, limitations, expectations, contributions and products.
Delivery of requested DEMs of AOIs to the partners

## Slide 55
Paul Morin
PGC PI/Director
lpaul@umn.edu
Mike Cloutier
ArcticDEM Contact for International Partners
clou0012@umn.edu
Polar Geospatial Center
www.pgc.umn.edu
@polargeospatial
/polargeospatial

## Slide 56
ArcticDEM Technical Details
Paul Morin and Mike Cloutier
Polar Geospatial Center
October 26, 2015

## Slide 57
The DigitalGlobe Satellite Constellation
WorldView-2
GeoEye
QuickBird
IKONOS
WorldView-3
WorldView-1

## Slide 58: Problems with the DEMs
~4m bias in all directions because of the RPCs
Holes in the DEMs
Water
Ice
Snow
This is a Digital Terrain Model - No bare ground
Derived from optical data

## Slide 59: Strategy
Process 2 coverages of 8m DEMs first
Identify what failed and why
Can the failures be fixed?
Process the rest
Develop automated methods for hole filling, applying ground control and mosaicking
Reapply as needed
Volume is key

## Slide 60
The ArcticDEM Domain

## Slide 61
SUPERCOMPUTING
hardware & infrastructure
Servers at OIT data center wrapped for cooling

## Slide 62: NSF High Performance Computing
About 40,000,000 Core hours Allocated

## Slide 63
g
Cray XE6/XK7 - 276 Cabinets
XE6 Compute Nodes
5,688 Blades – 22,640 Nodes – 362,240 Cores –
724,480 Integer Cores 4 GB per FP core
DSL
48 Nodes
MOM
64 Nodes
esLogin
4 Nodes
Import/Export
28 Nodes
Management Node
esServers Cabinets
HPSS Data Mover
50 Nodes
XK7 GPU Nodes
1056 Blades – 4,224 Nodes
33,792 Cores – 4,224 GPUs
Sonexion
25+PB online storage
144+144+1440 OSTs
BOOT
Nodes
SDB
Nodes
Network GW
Nodes
Unassigned
Nodes
LNET Routers
582 Nodes
InfiniBand fabric
Boot RAID
Boot Cabinet
SMW
10/40/100 Gb
Ethernet Switch
Gemini Fabric (HSN)
RSIP
Nodes
NCSAnet
Near-Line Storage
300+PB
Cyber Protection IDPS
NPCF
Notes: Blue Waters supersystem, Need to emphasize the unprecedented scale. Largest Cray, IE, HPSS, Lustre, Network. Hold performance discussion to later slides. Note all storage sizes are usable storage.

## Slide 64: Stereo Coverage by Year

## Slide 65: PGC’s Contribution
Processing the stereo imagery into DEMs
Tasking to continue to fill holes and continue the time series
Other automated post processing
  Ground control using LiDAR
  Mosaicking
PGC will not manually improve data products

## Slide 66: Next Steps
2m DSM of Alaska – Currently ~84% of the state has existing stereo
8m Circum-Arctic test
Begin development of circum-arctic ground control database
NGA is raising the priority of collection over stereo imagery holes.
Work with the arctic nations on their contributions including ground control, coastline, DEM improvement, etc.

## Slide 67: Ironies
North is better
Coastal is better
Remote is better
It is all about volume
Cloud cover assessment is often wrong
It is about having the data online
Networking, storage and compute is key

## Slide 68: What is SETSM?
Surface Extraction through Triangulated Irregular Network-based Search-space Minimization
Authored by Dr. Myoung-Jong Noh, Ohio State University
The main objective of SETSM is fully automatic and high quality stereoscopic DEM extraction from pushbroom (e.g. WorldView, GeoEye, etc.) satellite images.
No tuning parameters: fully adaptive match operations
No tie point selection: only sensor model needed.
No seed DEM: match refinement by sensor model bias correction.
No manual editing: effective blunder elimination and post-processing using only match-point density.

## Slide 69: How does SETSM work?
Three innovations make SETSM possible:
Object-Space matching using Vertical Line Locus (VLL)
Traditional “Area-space” matching: Given a point in one image, where is the corresponding or conjugate point in the second image?
Object-Space Matching: Given a planimetric location in object space (on the ground), what is the elevation that gives the best match between a pair of sub-image patches, obtained by projecting the candidate points into the images?
VLL Object-space matching allows for adaptive search space sizing based on geometry and relative sensor model accuracy. Also, the posted resolution of the DEM is the “true” resolution, unlike area-space matching.
Coarse-to-fine processing structure
Iterative refinement and adaptive adjustment of match constraints and blunder detection.
Sensor model Refinement
Bias in the sensor model are reduced through iterative refinement, enabling processing without a priori information (e.g. seed DEM or tie points).

## Slide 70: What does SETSM produce?
Gridded and gap-filled DEM
“Matchtag” Image with 1’s for pixels with matched points and 0’s for interpolated pixels.
16 bit orthorectified image at DEM resolution (not openly distributable currently)
Raw DEM
Matchtag Mask
Ortho Image

## Slide 71: What’s the data quality?
Raw DEM’s have systematic positional errors of up to several meters
  due to sensor model errors (Rational Polynomial Coefficients or RPCs)
  corrected with ground control (lidar, GPS points, etc)
The relative (point-to-point) error in the DEM is order decimeters
  this is the expected error after ground control is applied
Image edge effects, clouds, severe shadows and water bodies result in bad data
  these are effectively filtered using the matchtag field

## Slide 72: How is data quality improved?
Arctic tundra example
edge effects
lakes
Raw DEM (hillshade)
Ortho Image
matchtag field
point density field
Red = point density < 30%

## Slide 73: What Can You Offer?
Ground Control
Improvement of the DEMs
  Hole identification
  Hole filling
  Blunder editing
Staff for short-term detail at PGC in Minnesota

## Slide 74: Processing Strategy
We cannot manually examine 300,000 pairs
Use the processing of 8m DEMs to check the quality of the pair
When a 8m DEM succeeds process to 2m when more HPC time is available
PGC has enough time to produce 8m DEMS for ~150,000 – 17x17km pairs

## Slide 75: ArcticDEM Characteristics
File Format: 32 bit GeoTIFF
Projection: NSIDC Sea Ice Polar Stereographic North
  Note: forthcoming effort to mosaic DEM strips will be tiled and projected to UTM
Vertical Datum/Reference: WGS84 ellipsoidal (native SETSM output)
Elevation Units: meters
No Data Value: -9999
Initial data generated and archived according to the DigitalGlobe satellite stereopair “strip” used to create the terrain
  Typically around 17km x 120km, but a lot of variability
File Size
  2m Resolution: Approximately 1 MB per sqkm (~1 GB per 1000 sqkm)
  8m Resolution: Approximately 0.06 per sqkm (~65 MB per 1000 sqkm)
File naming
  Pipeline_Sensor_YYYYMMDD_Pair-ID1_Pair-ID2_Part#_Resolution_Component
  SETSM_WV01_20150215_102001003A308300_102001003BC43700_1_8m_dem

## Slide 76: Pocket Drive Contents (yours to keep)
ArcticDEM data
  DEM strips over AOIs requested through Tracy
    Canada, Finland, Sweden, Norway, Faroe Islands (2m & 8m resolution)
  Additional Data: Alaska Regions, Svalbard (8m resolution)
  Matchtag files
    Bitmask of pixels derived from stereo match (1) or interpolated (0)
Auxiliary Files Folder
  Shapefile of ArcticDEM regions being produced
  Shapefile index of DEM files
    Refer to “Pairname” field above to identify DEM/Matchtag files
SETSM_ASP_Components_Doc.pdf
  Explanation of output files generated from SETSM and ASP stereo pipelines
    Note: not all files will be included on the hard drive at this time

## Slide 77: General Notes and Comments
We ask that you not release the DEMs yet
Due to licensing, source stereo imagery used for production will not be available for distribution
  Metadata associated with the source imagery will be available
    Collection date, collection angles, image resolution, cloud cover, browse images

## Slide 78: Useful Partner Contributions
Control Sources to Enhance Accuracy
  LiDAR (airborne or terrestrial)
  InSAR Surveys
  GNSS ground surveys
  Cadastral Points
High Resolution Coastline Features
Large scale polygonal & linear hydrographic features (1:25,000 scale or better)
Feedback
  Recommendations
  Identification of problem areas (artifacts, voids, pits/spikes)
Post-processing & editing

## Slide 79: Next Steps
Metadata Generation and Indexing
  Auto-generated XML files describing data
  Polygonal coverage footprints
FTP delivery
  Folders set up by region
  PGC can notify Partner’s when new data becomes available
Discovery & Understanding of Auxiliary Partner Data Sources to Improve Terrain
Ongoing Gap/Cloud-Fill Image Tasking
Versioning
Re-ingest and re-distribution strategy of improved data

## Slide 80
Paul Morin
PGC PI/Director
lpaul@umn.edu
Mike Cloutier
ArcticDEM Contact for International Partners
clou0012@umn.edu
Polar Geospatial Center
www.pgc.umn.edu
@polargeospatial
/polargeospatial